## Slide 1: STM32 LED, Button, PWM, Analog Input, UART, FreeRTOS
18.10.2024
Student Lab 1

## Slide 2: Basic Knowledge
  STM32CubeMX and STM32CubeIDE
  Both software are tools from STMicroelectronics (www.st.com)
  STM32CubeMX
  STM32CubeMX - STM32Cube initialization code generator – STMicroelectronics
  STM32CubeIDE
  STM32CubeIDE - Integrated Development Environment for STM32 - STMicroelectronics
You will need ST account to access these software

## Slide 3: Basic Knowledge
  Development boards
  NUCLEO-G474RE from STMicroelectronics
NUCLEO-G474RE - STM32 Nucleo-64 development board with STM32G474RE MCU, supports Arduino and ST morpho connectivity – STMicroelectronics
with STM32G474RE MCU
STM32G474RE - Mainstream Arm Cortex-M4 MCU 170 MHz with 512 Kbytes of Flash memory, Math Accelerator, HR Timer, High Analog level integration - STMicroelectronics

## Slide 4: Basic Knowledge
Microcontroller: STM32G474RE
- Core: ARM Cortex-M4
- Frequency: 170 MHz
- Architecture: 32-bit RISC
Memory:
- Flash Memory: 512 KB
- SRAM: 96 KB
Peripheral / Communication Interfaces:
- SPI: Dual mode QuadSPI interface,
- UART/USART: 5 channels, including USB
- LIN: LIN support via USART
- I2C: 4 interfaces
- ADC: 5 x 12-bit ADCs, up to 42 channels
- DAC: 12-bit DAC, 7 channels
- GPIO: Up to 107 pins
- Timers: 17 timers
- DMA: 16 streams, 16-bit data bus
Operating System Support:
- FreeRTOS: Supported
Debugging and Programming:
- On-board Debugger: STLINK-V3E debugger/programmer
- IDE Compatibility: STM32CubeIDE, Keil MDK-ARM, IAR
Embedded Workbench
Expansion connectors:
- Arduino Uno V3 Connectivity
- ST morpho headers
Additional Features:
- CRC Calculation Unit
- True Random Number Generator

## Slide 5: Basic Knowledge: Nucleo board
User Button B1
User LED LD2

## Slide 6: Basic Knowledge: Nucleo board
Check the default jumpers and leave them as default!

## Slide 7: Basic Knowledge: Nucleo board

## Slide 8
Lab1 content
Lab1a: LED and Button from NUCLEO (Demonstration code from NUCLEO board)
Lab1b:
- LED and Button
- PWM and FreeRTOS
- Exercise 1 (combine LED, button, and PWM)
Lab1c:
- Analog Input (ADC)
- Exercise 2 (read potentiometer)
Lab1d
- UART
- Exercise 3 (display potentiometer/PWM value)

## Slide 9
Lab1a
LED and Button from NUCLEO
Notes: F:\AEE\AEE2\BSW\BSW Goals\ST firmware\StudentLab2024\Lab1a\Lab1a_LED_Button

## Slide 10: Lab1a: LED and Button from NUCLEO
In this lab, we will use the demonstration code that provided by NUCLEO board
We will learn how to open STM32CubeMX and generate code to STM32CubeIDE
We will learn to run the code in debug mode of STM32CubeIDE
Notes: F:\AEE\AEE2\BSW\BSW Goals\ST firmware\StudentLab2024\Lab1a\Lab1a_LED_Button

## Slide 11: Lab1a: LED and Button from NUCLEO
Open STM32MCubeMX
Click
Type
Notes: F:\AEE\AEE2\BSW\BSW Goals\ST firmware\StudentLab2024\Lab1a\Lab1a_LED_Button

## Slide 12: Lab1a: LED and Button from NUCLEO
Choose
Click
Notes: F:\AEE\AEE2\BSW\BSW Goals\ST firmware\StudentLab2024\Lab1a\Lab1a_LED_Button

## Slide 13: Lab1a: LED and Button from NUCLEO
Leave others as default and click
Notes: F:\AEE\AEE2\BSW\BSW Goals\ST firmware\StudentLab2024\Lab1a\Lab1a_LED_Button

## Slide 14: Lab1a: LED and Button from NUCLEO
Notes: F:\AEE\AEE2\BSW\BSW Goals\ST firmware\StudentLab2024\Lab1a\Lab1a_LED_Button

## Slide 15: Lab1a: LED and Button from NUCLEO
Check Pinout & Configuration that made by Nucleo board
Notes: F:\AEE\AEE2\BSW\BSW Goals\ST firmware\StudentLab2024\Lab1a\Lab1a_LED_Button

## Slide 16: Lab1a: LED and Button from NUCLEO
Notes: F:\AEE\AEE2\BSW\BSW Goals\ST firmware\StudentLab2024\Lab1a\Lab1a_LED_Button

## Slide 17: Lab1a: LED and Button from NUCLEO
Check Clock Configuration that made by Nucleo board
Leave everything as default
Notes: F:\AEE\AEE2\BSW\BSW Goals\ST firmware\StudentLab2024\Lab1a\Lab1a_LED_Button

## Slide 18: Lab1a: LED and Button from NUCLEO
Leave others as default
Notes: F:\AEE\AEE2\BSW\BSW Goals\ST firmware\StudentLab2024\Lab1a\Lab1a_LED_Button

## Slide 19: Lab1a: LED and Button from NUCLEO
Leave others as default and click
Notes: F:\AEE\AEE2\BSW\BSW Goals\ST firmware\StudentLab2024\Lab1a\Lab1a_LED_Button

## Slide 20: Lab1a: LED and Button from NUCLEO
Sometimes it will ask for downloading new package. Click Yes to continue
Click Open Project when this window appears
Choose or type workspace folder
Notes: F:\AEE\AEE2\BSW\BSW Goals\ST firmware\StudentLab2024\Lab1a\Lab1a_LED_Button

## Slide 21: Lab1a: LED and Button from NUCLEO
The project will be opened in STM32CubeIDE
Notes: F:\AEE\AEE2\BSW\BSW Goals\ST firmware\StudentLab2024\Lab1a\Lab1a_LED_Button

## Slide 22: Lab1a: LED and Button from NUCLEO
Check main.c, double click to open
To build project:
  Right click on the project name and choose Built Project
Notes: F:\AEE\AEE2\BSW\BSW Goals\ST firmware\StudentLab2024\Lab1a\Lab1a_LED_Button

## Slide 23: Lab1a: LED and Button from NUCLEO
From Console tab, it can be seen whether the project is built successfully or not
Notes: F:\AEE\AEE2\BSW\BSW Goals\ST firmware\StudentLab2024\Lab1a\Lab1a_LED_Button

## Slide 24: Lab1a: LED and Button from NUCLEO
From Console tab of STM32CubeIDE
To use serial print to monitor
Go to the Device Manager and check the STLink Virtual COM Port
Notes: F:\AEE\AEE2\BSW\BSW Goals\ST firmware\StudentLab2024\Lab1a\Lab1a_LED_Button

## Slide 25
Put connection name and COM settings
Notes: F:\AEE\AEE2\BSW\BSW Goals\ST firmware\StudentLab2024\Lab1a\Lab1a_LED_Button

## Slide 26: Lab1a: LED and Button from NUCLEO
Connect NUCLEO-G474RE to PC
Click Debug button
Leave everything as default and click
- Click Switch if this window appears
Notes: F:\AEE\AEE2\BSW\BSW Goals\ST firmware\StudentLab2024\Lab1a\Lab1a_LED_Button

## Slide 27
Choose the Console to monitor
Notes: F:\AEE\AEE2\BSW\BSW Goals\ST firmware\StudentLab2024\Lab1a\Lab1a_LED_Button

## Slide 28: Lab1a: LED and Button from NUCLEO
Click Resume button to run the code
Notes: F:\AEE\AEE2\BSW\BSW Goals\ST firmware\StudentLab2024\Lab1a\Lab1a_LED_Button

## Slide 29: Lab1a: LED and Button from NUCLEO
Observe on NUCLEO board:
  LD2 must lit (ON, green LED) in the beginning
  Every pressing of B1 (blue button), LD2 will be toggled (ON to be OFF, or OFF to be ON)
Notes: F:\AEE\AEE2\BSW\BSW Goals\ST firmware\StudentLab2024\Lab1a\Lab1a_LED_Button

## Slide 30
Lab1b
LED and Button
Notes: F:\AEE\AEE2\BSW\BSW Goals\ST firmware\StudentLab2024\Lab1b\Lab1b_LED_Button

## Slide 31: Lab1b: LED and Button
In this lab, we will set LED and button in STM32CubeMX, not using NUCLEO board setting
We will get familiar with HAL functions for LED and button
We will still use LD2 (PA5) as LED (GPIO output)
We will still use B1 (PC13) as button (GPIO EXTI13)
Notes: F:\AEE\AEE2\BSW\BSW Goals\ST firmware\StudentLab2024\Lab1b\Lab1b_LED_Button

## Slide 32: Lab1b: LED and Button
Open STM32MCubeMX
Click
Click
Notes: F:\AEE\AEE2\BSW\BSW Goals\ST firmware\StudentLab2024\Lab1b\Lab1b_LED_Button

## Slide 33: Lab1b: LED and Button
Notes: F:\AEE\AEE2\BSW\BSW Goals\ST firmware\StudentLab2024\Lab1b\Lab1b_LED_Button

## Slide 34: Lab1b: LED and Button
Notes: F:\AEE\AEE2\BSW\BSW Goals\ST firmware\StudentLab2024\Lab1b\Lab1b_LED_Button

## Slide 35: Lab1b: LED and Button
Notes: F:\AEE\AEE2\BSW\BSW Goals\ST firmware\StudentLab2024\Lab1b\Lab1b_LED_Button

## Slide 36: Lab1b: LED and Button
Notes: F:\AEE\AEE2\BSW\BSW Goals\ST firmware\StudentLab2024\Lab1b\Lab1b_LED_Button

## Slide 37: Lab1b: LED and Button
Fill with 170 and it will find the solution automatically
Notes: F:\AEE\AEE2\BSW\BSW Goals\ST firmware\StudentLab2024\Lab1b\Lab1b_LED_Button

## Slide 38: Lab1b: LED and Button
Notes: F:\AEE\AEE2\BSW\BSW Goals\ST firmware\StudentLab2024\Lab1b\Lab1b_LED_Button

## Slide 39: Lab1b: LED and Button
Our code must be put between:
/* USER CODE BEGIN XXXX */
and
/* USER CODE END XXXX */
HAL functions for GPIO can be found in file:
stm32g4xx_hal_gpio.c
Notes: F:\AEE\AEE2\BSW\BSW Goals\ST firmware\StudentLab2024\Lab1b\Lab1b_LED_Button

## Slide 40: Lab1b: LED and Button
In main.c
Build and debug code
Observe:
  LD2 must lit (ON, green LED) in the beginning
  Every pressing of B1 (blue button), LD2 will be toggled (ON to be OFF, or OFF to be ON)
Notes: F:\AEE\AEE2\BSW\BSW Goals\ST firmware\StudentLab2024\Lab1b\Lab1b_LED_Button

## Slide 41
Lab1b
PWM and FreeRTOS
Notes: F:\AEE\AEE2\BSW\BSW Goals\ST firmware\StudentLab2024\Lab1b\Lab1b_PWM_FreeRTOS1

## Slide 42: Lab1b: PWM and FreeRTOS
In this lab, we will set LED controlled by PWM in STM32CubeMX
We will use PA5 as TIM2_CH1. Timer 2 channel 1 will be set as PWM generator.
  F (PWM) = F (Clock) / ((Prescaler+1) (Period+1))
  We will use: 170MHz / (169+1)(9999+1) = 100 Hz
We will still use B1 (PC13) as button (GPIO EXTI13)
We will use FreeRTOS based code
Clock Configuration tab will be the same as previous example
Notes: F:\AEE\AEE2\BSW\BSW Goals\ST firmware\StudentLab2024\Lab1b\Lab1b_PWM_FreeRTOS1

## Slide 43: Lab1b: PWM and FreeRTOS
Notes: F:\AEE\AEE2\BSW\BSW Goals\ST firmware\StudentLab2024\Lab1b\Lab1b_PWM_FreeRTOS1

## Slide 44: Lab1b: PWM and FreeRTOS
Notes: F:\AEE\AEE2\BSW\BSW Goals\ST firmware\StudentLab2024\Lab1b\Lab1b_PWM_FreeRTOS1

## Slide 45: Lab1b: PWM and FreeRTOS
Select Timebase Source other than SysTick
for FreeRTOS based code
Notes: F:\AEE\AEE2\BSW\BSW Goals\ST firmware\StudentLab2024\Lab1b\Lab1b_PWM_FreeRTOS1

## Slide 46: Lab1b: LED and PWM
LD2 will dim based on PWM value.
In main.c
Build and debug code
Observe:
  LD2 must dim repeatedly OFF to ON
Notes: F:\AEE\AEE2\BSW\BSW Goals\ST firmware\StudentLab2024\Lab1b\Lab1b_PWM_FreeRTOS1

## Slide 47: Lab1b: LED, Button, and PWM
Exercise 1
Modify the code: Use both tasks (Task1 and Task2)
Task1 : Once button B1 is pressed, LD2 brightness will increase (min to max in 1s).
Task2 : When the brightness reaches maximum, in next pressed button of B1, LD2 brightness will decrease (max to min in 1s).
And so on…
Notes: F:\AEE\AEE2\BSW\BSW Goals\ST firmware\StudentLab2024\Lab1b\Lab1b_PWM_FreeRTOS_x

## Slide 48
Lab1c
Analog Input (ADC)
Notes: F:\AEE\AEE2\BSW\BSW Goals\ST firmware\StudentLab2024\Lab1c\Lab1c_ADC

## Slide 49: Lab1c: Analog Input (ADC)
In this lab, we will set analog input pins.
  Analog input is converted to digital using ADC
  We use 12-bit ADC (ADC value is 0 - 4095)
We will use PC0 and PC3 as analog input.
We will read voltages from PC0 and PC3
(using ADC polling conversion)
We will use FreeRTOS based code, the same as previous example
Clock Configuration tab will also be the same as previous example
Notes: F:\AEE\AEE2\BSW\BSW Goals\ST firmware\StudentLab2024\Lab1c\Lab1c_ADC

## Slide 50: Lab1c: Analog Input (ADC)
Notes: F:\AEE\AEE2\BSW\BSW Goals\ST firmware\StudentLab2024\Lab1c\Lab1c_ADC

## Slide 51: Lab1c: Analog Input (ADC)
Notes: F:\AEE\AEE2\BSW\BSW Goals\ST firmware\StudentLab2024\Lab1c\Lab1c_ADC

## Slide 52: Lab1c: Analog Input (ADC)
Notes: F:\AEE\AEE2\BSW\BSW Goals\ST firmware\StudentLab2024\Lab1c\Lab1c_ADC

## Slide 53: Lab1c: Analog Input (ADC)
In main.c
Notes: F:\AEE\AEE2\BSW\BSW Goals\ST firmware\StudentLab2024\Lab1c\Lab1c_ADC

## Slide 54: Lab1c: Analog Input (ADC)
Build and debug code
Add adc_raw and adc_mV in Live Expression
Resume code and observe the values of adc_raw and adc_mV in Live Expression (yellow means the data is changed)
Notes: F:\AEE\AEE2\BSW\BSW Goals\ST firmware\StudentLab2024\Lab1c\Lab1c_ADC

## Slide 55: Lab1c: Analog Input (ADC)
Connect PC0 pin to GND and PC3 to +3V3
Observe the values of adc_raw and adc_mV in Live Expression
  adc_raw[0] must be 0 and adc_raw[1] must be 4095
  adc_mV[0] must be 0 and adc_mV[1] must be 3300
Notes: F:\AEE\AEE2\BSW\BSW Goals\ST firmware\StudentLab2024\Lab1c\Lab1c_ADC

## Slide 56: Lab1c: LED, PWM, and Analog Input
Exercise 2
Modify the code: Use both tasks (Task1 and Task2)
  Connect potentiometer to PC0
  Task1: Read the ADC value of PC0
  Task2: Use the ADC value (0 – 4095) as value of PWM duty cycle (0 – 100%), observe LD2 (dimming based on potentiometer control)
The MCU uses 3.3V as supply voltage (VDDA).
Be careful to not exceed the voltage to analog input pins.
Notes: F:\AEE\AEE2\BSW\BSW Goals\ST firmware\StudentLab2024\Lab1c\Lab1c_ADC_x

## Slide 57
Lab1d
UART
Notes: F:\AEE\AEE2\BSW\BSW Goals\ST firmware\StudentLab2024\Lab1d\Lab1d_UART

## Slide 58: Lab1d: UART
In this lab, we will set UART communication.
We will use PA2 and PA3 as UART TX-RX, with interrupt.
We will use FreeRTOS based code, the same as previous example
Clock Configuration tab will be the same as previous example
Notes: F:\AEE\AEE2\BSW\BSW Goals\ST firmware\StudentLab2024\Lab1d\Lab1d_UART

## Slide 59: Lab1d: UART
Notes: F:\AEE\AEE2\BSW\BSW Goals\ST firmware\StudentLab2024\Lab1d\Lab1d_UART

## Slide 60: Lab1d: UART
Notes: F:\AEE\AEE2\BSW\BSW Goals\ST firmware\StudentLab2024\Lab1d\Lab1d_UART

## Slide 61: Lab1d: UART
In main.c
The serial monitor will display the initial message
and then the characters that we type will be displayed every 10 typed characters.
Notes: F:\AEE\AEE2\BSW\BSW Goals\ST firmware\StudentLab2024\Lab1d\Lab1d_UART

## Slide 62: Lab1d: UART
From Console tab of STM32CubeIDE
To use serial print to monitor in STM32CubeIDE
Go to the Device Manager and check the STLink Virtual COM Port
Notes: F:\AEE\AEE2\BSW\BSW Goals\ST firmware\StudentLab2024\Lab1d\Lab1d_UART

## Slide 63: Lab1d: UART
Put connection name and COM settings
The COM setting must be the same with UART settings
Notes: F:\AEE\AEE2\BSW\BSW Goals\ST firmware\StudentLab2024\Lab1d\Lab1d_UART

## Slide 64: Lab1d: UART
- Build and debug code
Notes: F:\AEE\AEE2\BSW\BSW Goals\ST firmware\StudentLab2024\Lab1d\Lab1d_UART

## Slide 65: Lab1d: UART
- Click Resume
- Type any character
The serial monitor will display the characters after we type 10 characters
Notes: F:\AEE\AEE2\BSW\BSW Goals\ST firmware\StudentLab2024\Lab1d\Lab1d_UART

## Slide 66: Lab1d: UART
Notes: F:\AEE\AEE2\BSW\BSW Goals\ST firmware\StudentLab2024\Lab1d\Lab1d_UART

## Slide 67: Lab1d: UART
If the serial monitor connection is already created, for the next debugging process, we can directly choose the connection by selecting from the button below.
Notes: F:\AEE\AEE2\BSW\BSW Goals\ST firmware\StudentLab2024\Lab1d\Lab1d_UART

## Slide 68: Lab1d: UART
Exercise 3
Modify the code: Use both tasks (Task1 and Task2)
  Display the value from potentiometer as value of PWM duty cycle (0-100%) to UART
Notes: F:\AEE\AEE2\BSW\BSW Goals\ST firmware\StudentLab2024\Lab1d\Lab1d_UART_x

## Slide 69
Thank you and good luck!